Physics of the Neutrino Factory and Related Long Baseline Designs
Or “an excuse to talk about neutrinos”
Jordi Burguet-Castell
Fri 7 Nov 2008

---
Outline
Introduction
The neutrino in the Standard Model
Neutrino Oscillations
Accelerator neutrino beams
The Neutrino Factory
Correlations and Degeneracies
SuperBeams combined with a Neutrino Factory
New experiments with non-conventional beams
Beta Beam
Electron-Capture Beam
Conclusions

---
Introduction
Discovery of the Neutrino
First postulated in 1930 by Pauli to save the conservation of energy and angular momentum in the b decay ( n → p e but the e doesn't have a fixed energy!)
In 1934 Fermi proposed his theory of
b decay. With it, Bethe and Peierls computed
that the probability of the neutrino interaction
with matter is extremely small (are they even detectable?)
Cowan & Reines detect in 1956 (anti)neutrinos, from a nuclear reactor through the reaction
(they detected two gammas coming from the positron annihilation and another gamma from the decay after the neutron is captured by the Cadmium).
{bar{%nu}}_e p toward n e^+.

---
Introduction
What are we made of?

---
Introduction
Neutrinos in the Standard Model
Where do neutrinos fit in the scheme of things?
Stable matter is made of this
An electron neutrino is the partner (in the weak isospin doublet) of an electron.
There are three species of neutrinos, partners to their respective leptons.
Neutrinos are only affected by the weak interaction (not the strong nor the electromagnetic).
Its spin is always oriented in the direction opposite to its velocity (it is “left-handed”).
In the SM it has no mass (there are no “right” components nR with which to couple).

---
Introduction
The Solar Neutrino Problem
Since the late 60s, neutrinos coming from the Sun were detected.
The Sun produces a lot of ne in the fusion reactions that take place in its core...
Neutrino spectra from different reactions in the Sun, as predicted by the Standard Solar Model
...but of the number expected from the Standard Solar Model only about 1/3 to 1/2 are detected!

---
Introduction
The Atmospheric Neutrino Problem
Not only the neutrinos from the Sun were puzzling.
Atmospheric neutrinos are produced in the collision of primary cosmic rays (typically protons) with nuclei in the upper atmosphere. This creates a shower of hadrons (mostly pions).
Neutrinos come mainly from:
%pi^+-. toward %mu^+-. %nu_%mu ({bar %nu}_%mu) newline %mu^+-. toward e^+-. %nu_e {bar %nu}_%mu ({bar %nu}_e %nu_%mu)
Absolute fluxes are hard to predict, but relative fluxes are easier, however...
left ( N_%mu over N_e right )_observed / left ( N_%mu over N_e right )_expected approx 0.6 !
Do nm disappear?
Do ne appear?
Roughly a flux ratio of
2-to-1 nm to ne expected

---
Introduction
Solution: oscillations
Electron neutrinos coming from the Sun are oscillating into other species.
Muon neutrinos produced in the atmosphere are also oscillating.
How? First, the weak interaction eigenstates do not coincide with the mass eigenstates (they are mixed, like the CKM mixing in the quark sector)
left ( matrix{ %nu_e ## %nu_%mu ## %nu_%tau } right ) = left ( matrix{U_{e1} # U_{e2} # U_{e3} ## U_{%mu 1} # U_{%mu 2} # U_{%mu 3} ## U_{%tau 1} # U_{%tau 2} # U_{%tau 3}} right ) left ( matrix{ %nu_1 ## %nu_2 ## %nu_3 } right )
PMNS matrix
Usual parametrization:
U = left ( matrix{1 # 0 # 0 ## 0 # cos %theta_{23} # sin %theta_{23} ## 0 # -sin %theta_{23} # cos %theta_{23}} right) left ( matrix{cos %theta_{color red 13} # 0 # sin %theta_{color red 13} e^{i color green %delta} ## 0 # 1 # 0 ## -sin %theta_{color red 13} e^{-i color green %delta} # 0 # cos %theta_{color red 13} } right ) left ( matrix{cos %theta_12 # sin %theta_12 # 0 ## -sin %theta_12 # cos %theta_12 # 0 ## 0 # 0 # 1} right )
Atmospheric
(nm disappearance)
Solar
(ne disappearance)
Interference
%theta_12 , %theta_23 , %theta_13 , %delta
And neutrinos must have different masses (and therefore, have mass)
%DELTA m^2_12 , %DELTA m^2_23
nu_evolution

---
Introduction
What remains to be known?
Different experiments are sensitive to different parameters:
%theta_13
%delta
%theta_12 , %DELTA m^2_12
%theta_23 , %DELTA m^2_23
Atmospheric n and accelerators
Solar n
and reactors
Accelerators and reactors
Accelerators
color red %theta_13 ? newline color green %delta ? newline color blue sign(%DELTA m^2_23) newline color blue %theta_23 octant ?
%theta_12 approx 34 newline %theta_23 approx 42 newline %DELTA m^2_12 approx 7.7 times 10^-5 eV^2 newline abs{%DELTA m^2_23} approx 2.3 times 10^-3 eV^2 newline %theta_13 < 10
What we don't know
What we know
Are neutrinos their own antiparticles (Dirac vs. Majorana)
Absolute Masses
If q13 > 0 and d ≠ 0, 180, then matter and antimatter behave differently for leptons (CP violation).

---
Conventional Neutrino Beams
The standard way to generate a neutrino beam:
Shoot protons against a target.
Use a magnetic horn to select (by charge) the generated hadrons (mostly pions)
Let them decay and either use directly the produced neutrinos (conventional beam) or capture the muons and let them decay to produce neutrinos.
%pi^+. toward %mu^+. %nu_{%mu} newline %pi^-. toward %mu^-. {bar %nu}_{%mu}
A conventional beam of mostly muon neutrinos
K^+. toward e^+. %pi^0 %nu_e newline K_L toward e^+-. %pi^-+. %nu_e ({bar %nu}_e)
%mu^+. toward e^+. %nu_e {bar %nu}_%mu newline %mu^-. toward e^-. {bar %nu}_e %nu_%mu
Also:
and

---
New Generation of Neutrino Beams
There is a new generation of facilities that explore the remaining unknown parameters :
We will see who they are and why they look for those oscillations.

---
The Neutrino Factory
So we wanted to measure q13 and d... and discover CP violation!
How is it best done?
oscgraph
An appearance experiment looking for
nm → ne
or
ne→ nm
where the solar and atmospheric terms interfere, is a good candidate.

---
The Neutrino Factory
Idea: create a background-free neutrino beam by accelerating muons and letting them decay.
%mu^+. toward e^+. %nu_e {bar{%nu}}_%mu
%mu^-. toward e^-. {bar %nu}_e %nu_%mu
Main advantages:
Without other neutrino species in the beam, an appearance experiment is very sensitive.
The neutrino energy spectrum is theoretically well known (less systematics)

---
Neutrino Factory Design
The basic details about the neutrino factory:
Proton driver 4 MW
Muon cooling and acceleration
E_%mu = 25 - 50 GeV
2x1020 useful muon decays per year
5 years running with each polarity

---
Golden Channel
What can you do with your muons?
color blue %mu^+. color black toward e^+. color red %nu_{e} color blue {bar{%nu}}_{%mu}
color blue {bar{%nu}}_%mu toward color blue %mu^+.
Disappearance
(sensitivity to q23 and Dm²23)
color red %nu_%mu toward color red %mu^-.
Appearance
(wrong-sign muons)
color blue %mu^-. color black toward e^-. color red {bar{%nu}}_{e} color blue %nu_{%mu}
“atmospheric”
“solar”
“interference”
In the appearance channel we are sensitive to q13 and d

---
Detector for a Neutrino Factory
To have information in the appearance and disappearance channel, one has to identify the muons and discern their charge.
A magnetized iron calorimeter with scintillator planes can do both.
MINOS
In the Deep Inelastic Scattering regime, cross sections grow linearly with energy.
High energies (> 10 GeV) increase the number of interactions and allow the energy to be reconstructed in such a detector.
MIND: a heavier MINOS-like detector

---
Matter Effects
To maximize the sensitivity we want to have as many appearance events as possible, and as dependent on d as possible.
In vacuum, the oscillation probability scales as E/L.
But in matter ne scatter with the electrons present in the medium and change the shape of the oscillation (MSW effect).
For <En> ~ 25 GeV... where is the oscillation maximum?
P_{%nu_e %nu_%mu} = s^2_23 sin^2 2 %theta_13 sin^2 {%DELTA m^2_23 L} over {4 E} + ...
oscgraph
So a Neutrino Factory works at a smaller E/L than it would for a shorter baseline to be in the oscillation peak.

---
Extracting the parameters
To extract the values of q13 and d one can perform a c2 fit of the (simulated) number of events to their expected value for all posible values of q13 and d.
The observables are the number of wrong-sign muons in serveral energy bins for both beam polarities:
With them, the c2 is obtained from:
Where the 2 Nbin x 2 Nbin covariance matrix is
c2 fit to simulated data
(contours show allowed regions at different CL)

---
Correlation between q13 and d
When the Neutrino Factory starts, d may have to be measured together with q13
Fits made with a single muon polarity and energy present a continuum of possible values for q13 and d...
As expected from the appearance formula:
When both polarities are used, the intersection presents a correlation: the knowledge of one parameter is affected by the (lack of) knowledge of the other.

---
Intrinsic Degeneracy
The allowed regions for each polarity may intersect in more than one place. If a different set of parameters can fit the same data we have degeneracies.
For a fixed energy and baseline, it is possible to find the fake values (q'13, d') by solving:
Fake solution
True solution
P_{%nu_e %nu_%mu}(%theta'_13, %delta') = P_{%nu_e %nu_%mu}(%theta_13, %delta) newline P_{{bar %nu}_e {bar %nu}_%mu}(%theta'_13, %delta') = P_{{bar %nu}_e {bar %nu}_%mu}(%theta_13, %delta)
This degeneracy is called the intrinsic degeneracy
(it is due to the behavior of the oscillation probability with q13 and d themselves)

---
Intrinsic Degeneracy
When doing simultaneous fits at L = 2810 km, for different central values of the oscillation parameters, we often find the intrinsic degeneracy.
It is not that important in the atmospheric regime (big q13, up to ~ 2º)
But it appears almost always in the solar regime
(small q13)

---
Eight-Fold Degeneracy
The fact that we don't know the sign(Δm223) produces an extra degeneracy.
It has also been identified that other fake solutions might appear from the unresolved
(fortunately, q23 seems to be close to p/4)
It is not expected that these degeneracies will be resolved before the time of the SuperBeam or of the Neutrino Factory. However, the appearance channel is sensitive to them, and it can be exploited.
color red { %theta_23 toward %pi / 2 - %theta_23 }
Both degeneracies can combine with the intrinsic degeneracy, separately or together, giving a full eight-fold degeneracy.

---
Possible Solutions
How can we solve those degeneracies?
We need to add more information!
Use 2 baselines (thus having a different E/L)
Take profit of the energy spectral information in the beam
Use another channel (like the silver channel, ne → nt, with another kind of detector)
Combine different facilities
We will further explore this option, combining a Neutrino Factory with a SuperBeam

---
SuperBeams: an Intermediate Step
The development of a Neutrino Factory requires the essentials of a Superbeam (a high intensity conventional neutrino beam) facility as an intermediate step.
A Superbeam by itself can largely improve our knowledge in
... though not much sensible to the CP violating phase.
%DELTA m^2_23 , %theta_23 , %theta_13
Superbeams are produced like conventional beams, just (much) more intense:
Typical source-detector distances are 150 – 700 km, in the peak of the neutrino oscillation.
%pi^+. toward %mu^+. %nu_{%mu} newline %pi^-. toward %mu^-. {bar %nu}_{%mu}
T2K neutrino fluxes

---
Water Cerenkov Detector
In a Superbeam, detection of low energy neutrinos (< 1 GeV) requires a massive target with high efficiency.
A search for ne appearance demands for low m misidentification and neutral current p0 production.
The technologies that can do that are water Cerenkov detectors and scintillator detectors.
Particle identification in a water Cerenkov:
Different pattern for showering (“e-like”) and non-showering (“m-like”) particles
Different Cerenkov opening angle
Delayed electron signature from the decay of a muon
m-like
e-like

---
Superbeam sensitivity on its own
Superbeams improve our knowledge of the atmospheric parameters thanks to the disappearance measurement.
They are good at measuring q13 to a certain point... and they do offer the possibility of CP violation discovery for high values of q13
Fits in the
plane after 5 years of the CERN-SPS Superbeam run
%DELTA m^2_23 , sin^2(2 %theta_23)
Fits in the q13, d plane

---
b-Beams
In a b-beam neutrinos are produced from the decay of accelerated b-unstable heavy ions. The resulting beam is pure (it only contains one neutrino species), and also the energy spectra is well known (low systematics, as in the case of a Neutrino Factory).
The b-Beam leverages existing CERN facilities: EURISOL and the SPS
Two ions are used:
    6He
 18Ne
b-Beam design
{bar %nu}_e
%nu_e
They are boosted to
g=E/m ~ 100, with E ~ 1 GeV
There is no need to identify the charge in the detector. A massive water Cerenkov detector is an ideal candidate.

---
b-Beam Sensitivity
b-Beams have good sensitivity to q13 and d,
especially for the high g option
(no ambiguities taken into account)
Sensitivity to q13
Sensitivity to CP violation

---
Electron-Capture Beam
Energy reconstruction in a b-Beam can be a problem. Another kind of neutrino beam, an Electron-Capture Beam uses boosted ions that undergo an e-capture transition (an atomic electron is captured by a proton and emits a ne). So:
There is only one neutrino species in the beam (like the b-Beam)
The beam is monochromatic (it's a two-body decay, the neutrino energy is fixed)
No need to reconstruct the energy. One can disentangle the different oscillation parameters by performing counting experiments at different g
Energy reconstruction can severely reduce the backgrounds though.
Tune different beams to the energies that better resolve q13 and d.
1018 ions/year
440 kton fiducial mass water Cerenkov detector at 130 km
5 years at g=195 and 5 years at g=90
Proposed setup:

---
EC-Beam Sensitivity
An EC-Beam can present good sensitivity to q13 and d
Sensitivity to q13
Sensitivity to CP violation
It is promising but:
It is not clear that ions will be able to keep one electron bound (partly ionized particles have a short vacuum life-time).
A realistic study of the expected ion flux is needed.
Systematics are low, but degeneracies could spoil its physics reach.

---
Conclusions
Neutrinos have mass – a discovery brought by neutrino oscillations.
A Neutrino Factory with neutrinos coming from muon decay at ~50 GeV and a baseline of ~3000 km, and looking for wrong-sign muons, is the most sensitive for the measurement of q13 and the discovery of CP violation in the leptonic sector.
To solve the correlations and degeneracies that appear in the joint measurement of q13 and d, more information is needed: use more than one baseline, exploit the silver channel, use energy spectral information and/or combine with other facilities.
Combination with SuperBeams, like the CERN SPL, can solve them up to q13 ~ 1º, and even for q13 ~ 0.5º only the octant may be a problem. Both experiments are complementary mainly due to their different E/L.
More recent proposals like BetaBeams or the Electron-Capture Beam can present a similar sensitivity and should be studied together.

---
The End

---
Backup Slides

---
Direct Neutrino Mass Searches
Searches with tritium
Astrophysical Limits
WMAP
2dF
Lyman-a forest data

---
b-Beams
We will consider the following setups:
  1. L=130 km at the optimal g accessible to the SPS
  2. g=150 (maximum at the SPS) at the optimal baseline
  3. g=350 at 730 km
In all cases, we assume a 10 years total run and the same number of decays per year:
    2.9x1018 6He decays
    1.1x1018 18Ne decays
The high g b-Beam produces a sizable fraction of non-quasielastic events in the detector.
To take into account the incorrectly reconstructed events we use migration matrices .
Reconstructed vs true energy for signal events

---
Neutrino Factory with Superbeam
For concreteness, the discussed results come from...
SETUPS:
Neutrino Factory with parent muon energy of 50 GeV and 2810 km baseline, running 5 years with m+ and 5 years with m.
Superbeam with the proposed CERN SPL accelerator, with average energy of 250 MeV and 130 km baseline, running 2 years with p+ and 8 years with p-

---
Solving the intrinsic degeneracy
The intrinsic solution is:
(vacuum approx)
Their different E/L makes the fake solution to be displaced in opposite directions... and the combination resolves the degeneracy!
Fits combining the results from the SPL-Superbeam and a Neutrino Factory at 2810 km. The fake intrinsic solutions completely disappear up to q13 ~ 0.5º

---
sign(Dm²23) degeneracy
With reversed sign for Dm²23, there exists new fake solutions for a fixed energy and distance:
P'_{%nu_e %nu_%mu}(%theta_13 ', %delta ') = P_{%nu_e %nu_%mu}(%theta_13, %delta) newline P'_{{bar %nu}_e {bar %nu}_%mu}(%theta_13 ', %delta ') = P_{{bar %nu}_e {bar %nu}_%mu}(%theta_13, %delta)
Matter effects allow a NuFact with L ~ 3000 km to resolve the degeneracy in the atmospheric region
Combination with a Superbeam resolves further, even in the solar regime

---
q23 → p/2 – q23 degeneracy
In the atmospheric regime, the fake solution due to the octant of q23 is clearly present in Superbeams, but less so in a Neutrino Factory.
P''_{%nu_e %nu_%mu}(%theta_13 ', %delta ') = P_{%nu_e %nu_%mu}(%theta_13, %delta) newline P''_{{bar %nu}_e {bar %nu}_%mu}(%theta_13 ', %delta ') = P_{{bar %nu}_e {bar %nu}_%mu}(%theta_13, %delta)
Superbeams
NuFact
The combination (not shown) solves them all

---
q23 → p/2 – q23 degeneracy
In the solar regime, the degeneracy severely affects the Neutrino Factory measurement, but the combination with a Superbeam solves it in most cases up to q13 ~ 0.5º
Combination
NuFact

---
3-families in the SM
Thanks to their contribution to the invisible Z decay width, we know that there are only 3 generations (but why?)

---
∗ Atmospheric νμ disappear (> 20σ) most likely to ντ
∗ K2K: accelerator νμ disappear at L ∼ 250 km
with E-distortion (∼ 2.5–4σ)
∗ MINOS: accelerator νμ disappear at L ∼ 735 km
with E-distortion (∼ 5σ)
∗ Solar νe convert to νμ or ντ (> 7σ)
∗ KamLAND: reactor νe disappear at L ∼ 200 km
with E-distortion (∼ 5σ CL)
Concha Gonzalez-Garcia @ NuFact08

---
Neutrino Masses

---
Other oscillation mechanisms
From Concha Gonzalez-Garcia

---
PMNS vs CKM

---
HARP's output
The cross section measurement in bins of momentum and angle translates
in an estimate of the parameters in the empirical Sanford & Wang formula:
The knowledge of this cross section is then exploited by other neutrino experiments.

---
NuFact Golden and Silver Channels
P_{%nu_e %nu_%mu ({bar %nu}_e {bar %nu}_%mu)} = . newline s_23^2 sin^2(2 %theta_13) left ( {%DELTA_13} over {B_{-+.}} right )^2 sin^2 left ( {B_{-+.} L} over 2 right ) newline + c_23^2 sin^2(2 %theta_12) left ( %DELTA_12 over A right )^2 sin^2 left ( {A L} over 2 right ) newline + J %DELTA_12 over A %DELTA_13 over B_{-+.} sin left ( {A L} over 2 right ) sin left ( {B_{-+.} L} over 2 right ) cos left ( +- %delta - {%DELTA_13 L} over 2 right )
P_{%nu_e %nu_%tau ({bar %nu}_e {bar %nu}_%tau)} = . newline c_23^2 sin^2(2 %theta_13) left ( {%DELTA_13} over {B_{-+.}} right )^2 sin^2 left ( {B_{-+.} L} over 2 right ) newline + s_23^2 sin^2(2 %theta_12) left ( %DELTA_12 over A right )^2 sin^2 left ( {A L} over 2 right ) newline - J %DELTA_12 over A %DELTA_13 over B_{-+.} sin left ( {A L} over 2 right ) sin left ( {B_{-+.} L} over 2 right ) cos left ( +- %delta - {%DELTA_13 L} over 2 right )

---
Resolving Degeneracies
Intrinsic: solved by spectrum information
sign(Dm²23): solved with matter effect
octant q23: identifying the solar oscillation effect

---
Correlations and Degeneracies
Correlations
The oscillation probability formulae entangle the parameters:
%theta_12 , %theta_23 , %theta_13 , %delta , %DELTA m^2_12 , %DELTA m^2_23
On trying to measure them simultaneously, the uncertainty for each one will depend on the (not completely known) value of the others.
The uncertainty in a single parameter can be taken from the projection. It will be bigger in general than the one if all the other parameters were fixed to theis central values.

---
b-Beam sensitivity to sign(Dm²23)
Region in which sign(Dm²23) can be measured, for q23 = 40.7 and Dm²23 > 0 (left) Dm²23 < 0 (right)

---
b-Beam sensitivity to the octant
Region in which the octant of q23 can be measured, for q23 = 40.7 (left) and q23 = 49.3 (right)

---
Degeneracies at a b-Beam
The intrinsic solution and its three images are strongly dependent on the neutrino energy and can be excluded when the energy dependence of the oscillation signal is significant.
Images of the true solution are energy independent and impossible to resolve unless there are additional measurements (like disappearance measurements or the silver channel) or when there are significant matter effects.

---
Costs (in M$)

---
Long Baseline Neutrino Experiments
MINOS
OPERA
ICARUS
T2K
NOvA

---
HARP
Contribution to MiniBooNE
Measurement of the p+ production cross section for a beam momentum of 8.9 GeV/c and a Be target.

---
HARP
Contribution to K2K
Prediction of the neutrino spectrum in SuperK and the near detector, using the HARP measurement of the p+ production for an Al target at 12.9 GeV/c beam momentum

---
HARP
Atmospheric Neutrinos
Production of p+ and p- in proton collisions with Carbon at 12 GeV/c

---
HARP
Neutrino Factory Target
Production of p+ and p- in p-Ta interactions at 3, 5, 8 and 12 GeV/c.
One of the candidates for the Neutrino Factory proton driver.

---
New generation of Neutrino Beams
Oscillation channel
Neutrino production
%pi^+. toward %mu^+. %nu_%mu newline %pi^-. toward %mu^-. {bar %nu}_%mu
%nu_%mu toward %nu_e newline {bar %nu}_%mu toward {bar %nu}_e
Superbeams
%mu^-. toward e^-. {bar %nu}_e %nu_%mu
{bar %nu}_e toward {bar %nu}_%mu
Neutrino Factory
%nu_e toward %nu_%mu
%mu^+. toward e^+. %nu_e {bar %nu}_%mu
%nu_e toward %nu_%mu newline {bar %nu}_%e toward {bar %nu}_%mu
b-Beam
.^{18}Ne toward %nu_e newline .^{6}He toward {bar %nu}_e